8X-RIPTIDE Assembler

# Preface & Introduction
Blah blah blah

# Assembler Features

# Command Line Interface

# Line Syntax
LABEL	MNEMONIC OPERANDS ; COMMENT
- Label – Must begin with an alphabetical character, can contain only letters and numbers, and must have no white-space preceding it on a line.
- Mnemonic – Must be preceded by white-space. Must be an instruction ("MOVE", "ADD", "AND", "XOR", "XEC", "NZT", "XMIT", "JMP", "CALL", "RET", "NOP") or assembler directive (“ORG”, “EQU”, “DATA”)
- Operands – Mnemonic-specific parameters
- Comment – Characters following a ‘;’ will be ignored by the assembler. Comments can be on their own line or on an instruction’s line, following the completed instruction syntax.
## Additional Line Structure
If a label appears on its own line, it will be stored by the assembler and mapped/attached to the following line. At most, one label can be attached to a line. If multiple labels appear before a mnemonic, only the last one will be valid.
LABEL
MNEMONIC OPERANDS ; COMMENT
In the following example, “LABEL” would not be valid for use and only “LABEL2” will be attached to the following mnemonic. Attempts to use “LABEL” will result in an error.
LABEL
LABEL2
MNEMONIC OPERANDS ; COMMENT
If a mnemonic appears at the beginning of the line (i.e. 0 indentation), the assembler will treat it as a label, likely resulting in an error.
LABEL
MNEMONIC OPERANDS

## Reserved Labels
The following keywords cannot be used as labels. Placing them at the beginning of a line results in a specific assembler directive. See (TODO: Link to directives).
- INCLUDE
- MACRO
- ENDMACRO
# Instruction Syntax
## NOP
NOP
Example:
NOP
## MOVE
MOVE S(R), D
Operands:
- S – Source register
- R – Rotate amount
- D – Destination register
Example:
MOVE R1(2), AUX
Notes:
The rotate amount, R, is an optional field.
E.g. “MOVE R1(0), AUX” is equivalent to “MOVE R1, AUX”
MOVE S, L, D
Operands:
- S – Source register
- L – Length
- D – Destination register
Example:
MOVE RIV3, 3, R6
## ADD
ADD S(R), D
Operands:
- S – Source register
- R – Rotate amount
- D – Destination register
Example:
ADD R1 (4), R3
Notes:
The rotate amount, R, is an optional field.
E.g. “ADD R1(0), R3” is equivalent to “ADD R1, R3”
ADD S, L, D
Operands:
- S – Source register
- L – Length
- D – Destination register
Example:
ADD R11, 4, LIV3
## AND
AND S(R), D
Operands:
- S – Source register
- R – Rotate amount
- D – Destination register
Example:
AND R1 (4), R3
Notes:
The rotate amount, R, is an optional field.
E.g. “AND R1(0), R3” is equivalent to “AND R1, R3”
AND S, L, D
Operands:
- S – Source register
- L – Length
- D – Destination register
Example:
AND R11, 4, LIV3
## XOR
XOR S(R), D
Operands:
- S – Source register
- R – Rotate amount
- D – Destination register
Example:
XOR R1 (4), R3
Notes:
The rotate amount, R, is an optional field.
E.g. “XOR R1(0), R3” is equivalent to “XOR R1, R3”
XOR S, L, D
Operands:
- S – Source register
- L – Length
- D – Destination register
Example:
XOR LIV7, 4, LIV3
## XEC
XEC I (S) [N]
Operands:
- I – Immediate/label
- S – Source register
- N – error checking, expected range of values (S), can’t be 0
Example:
XEC EX_LABEL (R3) [4]
Notes:
The expected range, “N”, is an optional field that tells the assembler that the expected values in (S) should vary in the range [0..N-1]. This means that the target location should vary in the range [I..I+N-1]. If the target location [I..I+N-1] can extend beyond the range of XEC, the assembler will emit a warning at assemble time.
If no value is provided for “N”, the assembler only checks that “I” is in range of XEC.
XEC I (S, L) [N]
Operands:
- I – Immediate/label
- S – Source register
- L – Length
- N – error checking, expected range of values (S), can’t be 0
Example:
XEC EX_LABEL (LIV4,3) [4]
Notes:
The expected range, “N”, is an optional field that tells the assembler that the expected values in (S) should vary in the range [0..N-1]. This means that the target location should vary in the range [I..I+N-1]. If the target location [I..I+N-1] can extend beyond the range of XEC, the assembler will emit a warning at assemble time.
If no value is provided for “N”, the assembler only checks that “I” is in range of XEC.
## NZT
NZT S, I
Operands:
- S – Source register
- I – Immediate/label
Example:
NZT R6, EX_LABEL
NZT S, L, I
Operands:
- S – Source register
- L – Length
- I – Immediate/label
Example:
NZT LIV5, 1, EX_LABEL
## CALL
CALL I
Operands:
I – Immediate/label
Example:
CALL EX_LABEL
## RET
RET
Example:
RET
## XMIT
XMIT I, D
Operands:
- I – Immediate/label
- D – Destination register
Example:
XMIT @027, IVL
XMIT I, D, L
Operands:
- I – Immediate/label
- D – Destination register
- L – Length
Example:
XMIT 03, LIV5, 3
## JMP
JMP A
Operands:
A – Address (13-bit field)
Example:
JMP EX_LABEL
# Declarations

# Directives